JDACTH Series

- Feature: Low ESR, Surface mounting, Reduced height, Wide temperature range

- Suitable for DC-DC converters, voltage regulators and decoupling applications

- Rate voltage: 2~25Vdc.

- Endurance: 1000hrs at 125℃

- RoHS Compliant

| Specifications |  |
| --- | --- |
| Item | Conditions | Characteristics |
| Category Temperature Range |  | -55 to +125 ℃ |
| Rated Voltage Range |  | 2 to 25Vdc |
| Capacitance Tolerance | at 20℃, 120Hz | ±20 % (M)；Y：+10 ~ -35%；K：±10 % |
| Leakage Current | at 20℃ after 2 minutes | I ≦ 0.1CV (2V.DC to 2.5V.DC) I ≦ 0.3CV (16V.DC to 25V.DC) I：Leakage Current(μA), C：Rated Capacitance(μF), V：Rated Voltage(V) |
| Surge Voltage | 15 to +35℃ | Rated voltage × 1.25 (2 V.DC to 16 V.DC) Rated voltage × 1.15 (20 V.DC to 25 V.DC) |
| Dissipation Factor (tanδ) | at 20℃，120Hz | ≦0.1 |
| Endurance | 125℃, rated voltage applied, 1000 hrs. | Appearance | No significant damage |
|  |  | Capacitance Change | ±20% of the initial value |
|  |  | Dissipation Factor | ( 200% of the initial specified value |
|  |  | Leakage Current | within the initial specified value |
| Damp Heat, Steady State | 60℃, 90 to 95%RH, 500 hrs. | Appearance | No significant damage |
|  |  | Capacitance Change | (2V.DC to 2.5V.DC)+70%, -20% of the initial value (16V.DC to 25V.DC) +60%, -20% of the initial value |
|  |  | Dissipation Factor | ( 200% of the initial specified value |
|  |  | Leakage Current | 2 V.DC to 2.5 V.DC within the initial specified value 10 V.DC to 25 V.DC (300% of the initial specified value |
| Surge Voltage | The capacitors shall be subjected to 1000 cycles each consisting of charge with the surge voltages, 125% rated voltage, at 15~35℃ for 30 seconds through a protective resistor(R=1KΩ)and discharge for 5min 30 seconds. | Appearance | No significant damage |
|  |  | Capacitance Change | ±10% of the initial value |
|  |  | Dissipation Factor | within the initial specified value |
|  |  | Leakage Current | within the initial specified value |
| Solderability | Pb-free solder Around 25% rosin melted ethanol or isopropylalcohol Temperature：245 ± 5 ℃ Immersing time：2 ± 0.5 s | More than 95% of outer terminal surface to be covered |
| Resistance to Solvents | Solvent：isopropylalcohol Immersing time：30 ± 5 s Room temperature | No significant damage and marking readable |

JDACTH Series

| Standard Ratings |
| --- |
| WV(VDC) | Cap(μF)@120Hz | tanδ Max. @120Hz | Leakage Current Max. (μA) | ESR Max. (mΩ) @100kHz | Ripple Current (A r.m.s) @100kHz | Part No. |
| 105℃ | 125℃ |  |  |  |  |  |  |
| 2 | 1.6 | 330 | 0.1 | 66.0 | 9 | 6.3 | JDACTH2R0S331E09 |
|  |  | 330 | 0.1 | 66.0 | 9 | 6.3 | JDACTH2R0S331E09Y |
|  |  | 330 | 0.1 | 66.0 | 6 | 7.5 | JDACTH2R0S331E06 |
| 2.5 | 2 | 330 | 0.1 | 82.5 | 9 | 6.3 | JDACTH2R5S331E09 |
|  |  | 330 | 0.1 | 82.5 | 9 | 6.3 | JDACTH2R5S331E09Y |
|  |  | 330 | 0.1 | 82.5 | 6 | 7.5 | JDACTH2R5S331E06 |
|  |  | 330 | 0.1 | 82.5 | 4.5 | 8.5 | JDACTH2R5S331E04 |
| 16 | 16 | 47 | 0.1 | 225.6 | 40 | 3.2 | JDACTH160S470E40 |
|  |  | 56 | 0.1 | 268.8 | 40 | 3.2 | JDACTH160S560E40 |
| 25 | 25 | 15 | 0.1 | 112.5 | 40 | 3.2 | JDACTH250S150E40 |
|  |  | 33 | 0.1 | 247.5 | 40 | 3.2 | JDACTH250S330E40 |

| Temperature Compensation Multipliers for Ripple Current |
| --- |
| Temperature | T≦45℃ | 45℃ ＜T≦ 85℃ | 85℃＜T≦105℃ | 125℃＜T |
| 2 V.DC to 2.5 V.DC | 1.0 | 0.7 | 0.25 | 0.25 |
| 16 V.DC to 25 V.DC | 1.0 | 0.8 | 0.5 | 0.25 |

PRODUCT IDENTIFICATION

| JD Coding | ACTH Product | 2R0 Rated Voltage 2R0: 2.0V | S Case Height S:1.9mm | 471 Capacitance 471=470µF | E06 ESR E06：6mΩ E04：4.5mΩ | □ Suffix for special code Y：Capacitance +10 ~ -35% K：Capacitance ±10% Blank space: Capacitance ±20 % |
| --- | --- | --- | --- | --- | --- | --- |

DIMENSIONS AND MARKING

| Case size | L | WA | WB | H | P |
| --- | --- | --- | --- | --- | --- |
| S | 7.3±0.3 | 4.3±0.3 | 2.4±0.2 | 1.9±0.3 | 1.3±0.2 |